## Slide 1: BASELABS DYNAMIC GRID

## Slide 2: BASELABS GmbH
Sensor Fusion Products for Automated Driving
Support ADAS / AD functions
  City AEBS, ACC
  Traffic Jam Pilot / Highway Pilot
  Automated Valet Parking
ASPICE / ISO26262 compliant
Capable of running on Off-the-shelf CPUs

## Slide 3: BASELABS Perception Stack
BASELABS
Environment model
Dynamic objects
Grid map
Free space polygon
Parking spots
High Resolution Radar
Radar Detections
Smart Radar objects
Camera Bounding Boxes
Camera Semantic information
Camera point cloud
Lidar Point Cloud
Smart Lidar Objects
Lidar Cluster

## Slide 4: AUTOMATED VALET PARKING

## Slide 5: Requirements for Perception System for Automated Valet Parking

## Slide 6: Existing Sensor Fusion Solutions
Existing Sensor Fusion Solutions work well for:
  Well-structured environments
  Similar Traffic Participants
  Limited number of scenarios
  Assisted Parking
  Highway AEBS / ACC
  Lane Keep, Lane Departure Warnings
2 Main components of Existing solutions
Dynamic Object Fusion
Static Grid Fusion

## Slide 7: Dynamic Object Fusion
Required Low-resolution Sensor Inputs
Requires priori known object types
Based on Kalman filter – Unimodal, Gaussian, Non-Linearity limitations
Well suited for large distance tracking of Dynamic objects
Limited performance for near distance and extended objects
No support for static environments

## Slide 8: High Resolution Sensor Data
Range, Azimuth and Doppler velocity
Large number of detections per objects
Detection-level output for low-level fusion
Radar Measurements
Dense Camera Detections
Semantic annotation and / or depth
Pixel level class and / or depth information

## Slide 9: Limitations of Dynamic Object Fusion
Limited performance for close-range and extended objects
Requires clustering of high-res sensor data
  Prone to errors due to early decision on data association
Required prior known object types
  Inherent risk to miss unknown dynamic objects

## Slide 10: Static Grid Fusion and its limitations
Static grid map contains static objects only
  Results in false negatives for free space
Workaround : Exclusion of measurements from dynamic objects
  Error propagation from dynamic object fusion
  High risk to fail in challenging scenarios

## Slide 11: Perception System for Next Generation ADAS / AD
Provides Object Extensions
Object Motion Prediction
Provides static objects
Provides free space
Supports unknown object types
Supports high-resolution sensor inputs
Current solutions features
Mismatch b/w problem and solution

## Slide 12: Dynamic Grid Fusion
Low level sensor fusion approach without early clustering
Integrated estimation of static and dynamic objects
No error propagation due to early decision
Supports high-resolution sensor inputs
Support for unknown object types
Fewer modelling assumptions

## Slide 13: Dynamic Grid
First parent – Static occupancy grid
Second parent – Particle filtering on dynamic objects

## Slide 14: Dynamic Grid
Allows for additionally fusing Semantic information

## Slide 15: Software Stack for L4 Parking (SOTIF consideration)

## Slide 16: Dynamic grid using Radars + Cameras

## Slide 17: Dynamic grid Advantages
High Detection Rate
  By Low-level sensor fusion without object extraction
Low False Alarm Rate
  By Integrated estimation of static and dynamic objects
Runs on Automotive CPUs
  By Minimizing particles in static areas

## Slide 18: References
Baselabs Automated Parking webinar
Sensor Fusion Hub Baselabs
Sensor Fusion Literature
Next-gen Sensor Fusion Baselabs YT video

## Slide 19: Backup slides

## Slide 20: Dynamic grid Advantages

## Slide 21: Levels of Automated Parking